## Slide 1
GRADE 6 SCIENCE
Lab Safety
How to stay safe in the science lab
mrzocchi.com

## Slide 2
Key Vocabulary
Hazard
Something that could cause harm — chemicals, heat, sharp objects.
Risk
The chance that a hazard will actually cause harm.
PPE
Personal Protective Equipment — goggles, gloves, lab coat.
Safety Symbol
A warning picture on chemicals or equipment.
MSDS
Material Safety Data Sheet — information about a chemical.
First Aid
Immediate help given when someone is hurt.

## Slide 3
General Lab Rules
Always wear safety goggles when using chemicals or heat.
Tie back long hair. Remove dangling jewellery.
Never eat, drink, or taste anything in the lab.
Walk — never run — in the science lab.
Report ALL spills, breakages, and injuries to your teacher immediately.
Know where the fire extinguisher, first aid kit, and eye wash station are.

## Slide 4
Hazard Symbols You Must Know
Danger Symbols
🔥 Flammable — catches fire easily
☠️ Toxic — can cause serious harm or death
⚠️ Irritant — can damage skin or eyes
🧪 Corrosive — destroys skin and metals
What To Do
Read the label BEFORE using any chemical.
Ask your teacher if you are unsure.
Use the smallest amount needed.
Wash hands after every experiment.

## Slide 5
Using a Bunsen Burner
Step 1: Check the rubber tube is connected tightly — no cracks.
Step 2: Close the air hole. Light the match FIRST, then turn on the gas.
Step 3: Yellow flame = safety flame (visible but cooler).
Step 4: Open the air hole = blue flame (hotter, for heating).
Step 5: When finished, close the air hole, turn off gas, let it cool.

## Slide 6
What If Something Goes Wrong?
Chemical splash in eyes → Use the eye wash station for 15 minutes.
Burn from heat → Run cold water over it for 10 minutes.
Chemical spill → Tell your teacher. Do NOT try to clean it yourself.
Broken glass → Do NOT pick it up with hands. Use a dustpan.
Fire → Tell your teacher. Walk to the exit calmly.

## Slide 7
Check Your Understanding
☐
I can name 3 general lab safety rules.
☐
I can identify at least 4 hazard symbols.
☐
I know how to light a Bunsen burner safely.
☐
I know what to do if there is a chemical spill.
☐
I can explain the difference between a hazard and a risk.

## Slide 8
Review & Practise
Use the Self-Quiz, Review Games, and Practice Builder to test yourself.
mrzocchi.com