## Slide 1
GRADE 6 SCIENCE
Measurement & Units
Measuring accurately in science
mrzocchi.com

## Slide 2
Key Vocabulary
SI Units
Standard International units used worldwide — metres, grams, seconds.
Accuracy
How close your measurement is to the true value.
Precision
How close your repeated measurements are to each other.
Meniscus
The curved surface of a liquid in a measuring cylinder.
Anomaly
A result that does not fit the pattern — an outlier.

## Slide 3
SI Units You Must Know
Quantity | Unit | Symbol | Equipment
Length | metre / centimetre | m / cm | Ruler / tape measure
Mass | gram / kilogram | g / kg | Electronic balance
Volume | millilitre / litre | mL / L | Measuring cylinder
Temperature | degrees Celsius | °C | Thermometer
Time | seconds / minutes | s / min | Stopwatch
Force | Newton | N | Newton meter

## Slide 4
How to Measure Volume Correctly
Place the measuring cylinder on a flat, level surface.
Pour the liquid slowly until near the desired amount.
Your eyes must be LEVEL with the liquid surface.
Read from the bottom of the meniscus (curved surface).
The meniscus curves down for water — read the lowest point.
Record the value with the correct unit (mL).

## Slide 5
Accuracy vs Precision
Accurate
Close to the TRUE value.
Like hitting the bullseye.
Need to know the real answer to check.
Improved by using better equipment.
Precise
Measurements are close TOGETHER.
Like all darts in the same spot.
Does NOT mean correct — can be precisely wrong.
Improved by careful technique.

## Slide 6
Common Measurement Mistakes
Parallax error: reading at an angle instead of eye level.
Zero error: not resetting the scale to zero before measuring.
Rounding too early: record the full reading, round later.
Wrong units: always include the unit with every measurement.
Only measuring once: take at least 3 readings and find the mean.

## Slide 7
Check Your Understanding
☐
I can name the SI unit for length, mass, volume, and temperature.
☐
I can read a measuring cylinder correctly (meniscus).
☐
I can explain the difference between accuracy and precision.
☐
I can identify common measurement errors.

## Slide 8
Review & Practise
Use the Self-Quiz, Review Games, and Practice Builder to test yourself.
mrzocchi.com