## Slide 1
GRADE 7 SCIENCE
Using Microscopes
Seeing the invisible world
mrzocchi.com

## Slide 2
Key Vocabulary
Microscope
An instrument that magnifies small objects so we can see them.
Magnification
How many times bigger the image appears.
Objective Lens
The lens closest to the specimen. Different powers: ×4, ×10, ×40.
Eyepiece Lens
The lens you look through. Usually ×10.
Specimen
The sample you are looking at under the microscope.
Slide
A thin glass plate that holds the specimen.

## Slide 3
How to Use a Microscope
1. Start with the LOWEST power objective lens (×4).
2. Place the slide on the stage, secured with clips.
3. Use the COARSE focus wheel to get a rough focus.
4. Switch to higher power (×10, then ×40) for more detail.
5. Use the FINE focus wheel for a sharp image.
6. ALWAYS start on low power — never start high!

## Slide 4
Calculating Magnification
Total magnification = eyepiece lens × objective lens.
Example: ×10 eyepiece × ×40 objective = ×400 magnification.
This means the image appears 400 times bigger than real life.
Light microscopes: up to ×1500 magnification.
Electron microscopes: up to ×2,000,000 magnification!

## Slide 5
Check Your Understanding
☐
I can label the parts of a light microscope.
☐
I can calculate total magnification.
☐
I can prepare a microscope slide.
☐
I know to always start on the lowest power objective.

## Slide 6
Review & Practise
Use the Self-Quiz, Review Games, and Practice Builder to test yourself.
mrzocchi.com